## Slide 1
Site characterization in New England using high resolution geology maps and a subregion grouping layer
Marshall Pontrelli1, Dr. Laurie Baise2, Dr. John Ebel3
1PhD Candidate (Tufts), 2Professor and Chair (Tufts), 3Senior Research Scientist (Boston College)
Marshall Center, Tampa Bay, FL, 33620, USA
ESSA annual meeting 10/25/2022
Research supported by USGS Award #s G20AP00040 and G20AP00040

## Slide 2
Presentation structure
1
Site response
Motivation
Layer-over-halfspace model
Introduction
Results
Summary and conclusion
Data
4. f0, Vsavg , and surficial geology database
Methods
Subregion development and map
f0 distribution development
Vsavg distribution development

## Slide 3
Site Response
Figure 2. Mexico City 1985
Figure 1. Loma Prieta 1989
Figure 3. One dimensional site response analysis schematic.
Figure 4. Suite of transfer functions from a soil site in Mexico City
2
Introduction

## Slide 4
Table 1. Vs30 based site class definitions.
Seismic Site Classification
3
Introduction

## Slide 5
Motivation
Existing New England site response models:
Figure 5. Slope-based Vs30 site class map of New England from Wald and Allen (2007)
Figure 6. Geology-based site class map of New England from Becker et al. (2011)
Figure 7. f0, Vsavg and geology-based site class map of New England from Pontrelli et al. (2022)
4
Introduction

## Slide 6
Where existing models can be approved upon
-Wald and Allen (2007) uses global data to develop Vs30-slope relationship – at the local and regional scale, this relationship will change based on local soil properties and basin geometries. The paper states: “[m]aps of seismic site-conditions on regional scales are relatively rare since they require substantial investment in geological and geotechnical data acquisition and interpretation”. This work is an attempt to make that investment.
5
Introduction
-Pontrelli et al. (2022) takes depth into account by using geophysical (f0) measurements but uses lower resolution geologic maps and doesn’t take into account depth variations between basins, only looking for variation across geologic units. Additionally, the methodology doesn’t propagate shear wave velocity uncertainty, only f0 uncertainty.
-Becker et al. (2011) uses local surficial geologic maps to map geologic units straight onto seismic site classes. This works well in terms of resolution but does not take into account depth – an essential variable in Vs30 calculations. In their model, if a surficial material is mapped as a marine clay, it will be a site class E soil no matter the depth.

## Slide 7
In this work we:
-Develop site characterization maps of New England by developing distributions of f0, Vsavg, and Vs30 across the region.
6
Introduction
Research question: What are the mean and standard deviation values of the distributions of f0, Vsavg, and Vs30 in New England?
-Use the highest available surficial geologic data available.
-Create a subregion grouping layer using a digital elevation model to subdivide our geophysical database, reducing dispersion in the parameter distributions.
-Develop distributions of f0 and Vsavg using subregions and propagate these distributions through the layer-over-halfspace model to create Vs30 distributions.

## Slide 8
Layer-over-halfspace model
7
Vsavg
ds
30 m
dR
VR
Figure 8. Relationship between f0 and Vs30 for the 4 Vsavg estimates of the 7 surficial units in the study.
Derivation is in Hassani and Atkinson (2016)
Relationship is valid when ds < 30 m. When ds > 30 m, Vs30 =Vsavg
Introduction

## Slide 9
Propagating uncertainty through the layer-over-halfspace model
8
Figure 9. f0 and Vsavg distribution inputs for Boston Basin artificial fill and the accompanying Vs30 distribution output.
Introduction
a)
b)
c)
d)

## Slide 10
Data to develop the f0 and Vsavg distributions
Figure 10. Final geology map developed from the state geological databases.
Figure 11. Spatial distribution of the HVSR database developed in this study.
Figure 12. a) Locations of shear wave velocity profiles in the study
9
Data

## Slide 11
Subregion development
Figure 13. Demonstration of the process used in this study to create subregion polygons.
10

## Slide 12
Developing f0 distributions
Figure 14. Geology of the Boston Basin with f0 stations overlain.
Figure 15. Distributions of Boston Basin artificial fill and alluvium/outwash f0 station values.
Table 2. Example of two rows of the output table from the grouping of f0 values in the Boston Basin.
11
Methods

## Slide 13
Developing Vsavg distributions
Figure 16. The 40 Vsavg values grouped by surficial geology with the selected mean value shown in red and the selected standard deviation value plus and minus the mean shown in blue.
Figure 17. The 6 distributions used for the eight surficial units in the study.
12
Methods

## Slide 14
f0 grouping distributions in each geology and subregion
Figure 18. Box and whisker plots of the f0 distributions of each subregion grouped by surficial geologic unit. This figure allows to compare across the same geology between different subregions, (e.g. a Maine coast fine and a Boston Basin fine).
13
Results

## Slide 15
Mapping Vs30 mean and standard deviation
14
Figure 19. Map of Vs30 mean.
Figure 20. Map of Vs30 std.

## Slide 16
Summary and conclusion
-Using the methodology presented here one can develop distributions of f0 and Vsavg from measurements, surficial geology and a subregion grouping layer and propagate that uncertainty to a computation of a distribution of Vs30.
-In New England, the lowest Vs30 mean regions are Cape Cod and Long Island, the Boston Basin, the Connecticut River Valley, and the Champlain Sea sediments.
-Vs30 calculations using the layer-over-halfspace model are very sensitive to f0 (depth) – when depth is greater than 30 m, Vs30 = Vsavg and where it is less than 30 m, the value changes significantly depending on the depth to the impedance contrast. This has implications in geology-based site classification – even soft soils have high Vs30 values when the deposit is shallow.
15

## Slide 17
16
References
Becker, L.R., Fratto, E.S., Patriarco, S.P., Marvinney, R.G., Mabee, S.B., Thomas, M.A. (2001) Utilizing the Surficial Geology of the Northeast United States to Improve NEHRP Site Effect Classifications in HAZUS-MH: Collaborative Research with NESEC and the NESEC State Geologists. U.S Geological Survey National Earthquake Hazard Reduction Program Award No. G10AP00014.
Hassani, B., Atkinson, G.M. (2016) Applicability of the Site Fundamental Frequency as a VS30 Proxy for Central and Eastern North America. Bulletin of the Seismological Society of America 2016; 106 (2): 653–664. doi: https://doi.org/10.1785/0120150259
Pontrelli, M.A., Baise, L.G., Ebel, J.E. (2022) Site Characterization Maps of New England Based on Local Geophysical and Geological Data. (In review in Engineering Geology). DOI: https://dx.doi.org/10.2139/ssrn.4214053
Wald, D. J., and Allen, T. I., 2007, Topographic slope as a proxy for seismic site conditions and amplification, Bulletin of the Seismological Society of America, 97, no. 5, 1379-1395. https://doi.org/10.1785/0120060267
We’d like to acknowledge Dr. Steve Mabee of UMASS Amherst for his HVSR data and shear wave velocity estimates and Dr. Weiwei Zhan at Tufts for his help propagating uncertainty through the layer-over-halfspace model

## Slide 18
Thank you
Questions?

## Slide 19
Handling groupings with little data in them
Extra
Create general “soft” geology distributions and use their mean and standard deviation when a grouping has few f0 stations.
17
Figure 20. Histograms and theoretical PDFs of the “soft” geologies of each subregion. “Soft” geologies are all units that are not defined as “till”.

## Slide 20
Discussion
Table 3. Several rows from the final output table of the analysis with Vs30 and depth means for the significant units of each of the subregions. Note that there are 39 of these rows for each of the geologic units in each of the subregions.
18
Extra

## Slide 21
Extra
Issue with Vs30 distribution
19
Figure 22. Relationship between f0 and Vs30 is not linear - where the mean depth of the unit is around 30 meters, the distributions become skewed.
Figure 21. Mean depth vs Vs30 distribution skewness. As the mean depth approaches 30 m, the distribution skewness approaches a maximum.
Depth = 30 m

## Slide 22
Analytical solution to the layer-over-halfspace model reducing computation (work in progress, derivation by Dr. Weiwei Zhan)
-
Where
(from data)
(from data)
(estimate)
(estimate)
Extra
20

## Slide 23
Vs30 outputs from the analytical solution
(from solution)
(from solution)
Extra
21